## Slide 1: Satellite View of the New PM2.5 Health Standard
Shobha Kondragunta (NOAA)
Michael Cheeseman, Hai Zhang, Pubu Ciren (IMSG at NOAA)

## Slide 3: VIIRs smoke/dust-free PM2.5 shows many regions in excess of the new NAAQs during the 2019-2021 period
Notes: Southeastern US exceedances may be driven by combination of local sources and optically thin transported smoke/dust that isn’t captured

## Slide 4: VIIRs smoke/dust-free PM2.5 shows many regions in excess of the new NAAQs during the 2019-2021 period
Increase from 1.6 million people to 65 million people above the NAAQs during 2019-2021
Notes: Southeastern US exceedances may be driven by combination of local sources and optically thin transported smoke/dust that isn’t captured

## Slide 5: VIIRs smoke/dust-free PM2.5 shows many regions in excess of the new NAAQs during the 2019-2021 period
Southeastern exceedances may be driven by combination of smoke/dust transport, sulfate aerosols, and secondary organic aerosol (SOAs) formation
Notes: Southeastern US exceedances may be driven by combination of local sources and optically thin transported smoke/dust that isn’t captured

## Slide 6: Future smoke/dust events could lead to substantial number of NAAQs exceedances
Notes: Southeastern US exceedances may be driven by combination of local sources and optically thin transported smoke/dust that isn’t captured

## Slide 7: Thus, smoke/dust events will likely drive increased demand for counties to produce EERs

## Slide 8: AirFuse A multi-pollutant fusion system
Shobha Kondragunta3,4
Co-authors: Barron H. Henderson1,4 and Phil Dickerson1,4 Pawan Gupta2,4, Yang Liu4,5, Alqamah Sayeed, Hai Zhang3,4, Janica Gordon5, Halil Cakir1, Brett Gantt1, Benjamin Wells1, Marcus Proctor6,7, Steven Proctor6,8, Youngsun Jung9, and the HAQAST AirNow Teams4
1US EPA Office of Air Quality Planning and Standards; 2National Aeronautics and Space Administration; 3National Oceanic and Atmospheric Administration / National Environmental Satellite, Data, and Information Service; 4NASA Health and Air Quality Applied Sciences Team and Tiger Teams; 5North Carolina Agricultural and Technical State University; 6AirNow Data Management Center; 7Tantus Technologies Inc.; 8GoldSystems Inc.; 9National Oceanic and Atmospheric Administration / National Weather Service
Disclaimer: The views expressed in this presentation are those of the authors and do not necessarily reflect the views or policies of the U.S. Environmental Protection Agency.

## Slide 9: GOES-PM25
Sayeed et al: Deep Neural Network bias corrections.
O'Dell et al.: Public Health Benefits from Improved Identification of Severe Air Pollution Events with Geostationary Satellite Data, submitted to GeoHealth, 2023.
Zhang et al.: Nowcasting Applications of Geostationary Satellite Hourly Surface PM2.5 Data. Weather and Forecasting, 37(12), 2313-2329, 2022. doi: 10.1175/WAF-D-22-0114.1
Bratburd et al.: Air Quality Data When You Need It: Incorporating Satellite Data Updates into AirNow, EM Plus, 2022.
Zhang and Kondragunta.: Daily and Hourly Surface PM2.5 Estimation From Satellite AOD, Earth Space Sci, 8, doi: 10.1029/2020EA001599, 2021.
https://haqast.org/tiger-teams/#2021-tiger-teams
Hourly product with gaps
DNN Bias Correction
2024 Team led by Yang Liu
Notes: Geostationary satellites are home bodies while polar satellites are globe trotters.
  Geostationary Operational Environmental Satellites (GOES) stare at the US all day long.
  Not like polar satellites passing once at 10am and once at 2pm (if you have two satellites)
From an US perspective, GOES satellites view the western US from the pacific and the eastern US from the atlantic.
Shobha Kondragunta and Hai Zhang fused with AirNow monitors by a geographic weighted regression.
Pawan led a tiger team to connect that data back to EPA.
  There are a lot of technical details, but the upshot is simple.
  We extensively evaluated the data, applied machine learning corrections, and we’re putting that data into various airnow systems like AirNowTech.
This is a great idea: federal agencies working together to provide tangible benefits to the American people from satellite data.
  This project is taking that data a step further.
  We’re going to bring the satellite data

## Slide 10: GOES-PM25 in https://airnowtech.org/
Login
Choose Navigator
Choose Data Fusion tab.
Select the GOES Layer
Green/Red indicates hour availability
Thanks AirNow team!

## Slide 11: AirFuse: Bias Correction Ensemble
YG = f(mod, GOES-PM)
YA = f(mod, AirNow)
YP = f(mod, PurpleAir)
GOES-PM Bias
NAQFC & GOES
aYA + pYP + gYG
Layer “correct” the NOAA forecast (NAQFC) by interpolating bias
One layer from AirNow monitor (YA) observations:
  Regulatory grade hourly observations paired with collocated grid cell.
  Voronoi interpolation to account for network spatial structure.
One layer from PurpleAir (YP) observations:
  Low-cost sensors corrected (Barkjohn 2021) then averaged in grid cells.
  Voronoi interpolation to account for network spatial structure.
One layer from GOES-PM25 (YG) “observations”
  GOES-R AOD regression with machine learning correction.
  Not clustered like monitors, so simple inverse distance interpolation.
Layer weights (a, p, g) a function of distance to obs and uncertainty.
Final Fused
Hatches: GOES-PM
YA
YP
YG
Notes: Hatches: GEOS

## Slide 12: AirFuse in https://airnowtech.org/
Currently includes AirNow and PurpleAir
PM25:
  Currently uses NAQFC, AirNow and PurpleAir only
  GOES-PM25 incorporation in AirFuse still under testing
Ozone:
  Currently uses NAQFC and AirNow only
Thanks AirNow team!