## Slide 1: Supporting Geostationary Observations from TEMPO and GeoXO: High-Resolution Surface Measurements from NOAA's ARC Mobile Lab
Xinrong Ren1, Phil Stratton1,2, Jiayang Sun1,2, Paul Kelley1,2, Winston Luke1, Russ Dickerson2, Zigang Wei3, Shobha Kondragunta3, and Joel Dreessen4
          1NOAA/OAR/Air Resources Lab
          2University of Maryland
          3NOAA/NESDIS/Center for Satellite Applications and Research
          4Maryland Department of Environment

## Slide 2: NOAA’s ARC Mobile Lab Team and Instrument Suite
Xinrong Ren - NOAA ARL
Paul Kelley - NOAA ARL
Jiayang Sun - U. of MD
Hannah Daley - U. of MD
Phil Stratton - NOAA ARL
An Instrumented Chevy Suburban
3 EcoFlow battery generators with a capacity of 10.8 KWh
8-10 hours of measurement
Two inlets, one for gases, the other for aerosols
Winston Luke - NOAA ARL

## Slide 3
NOAA’s ARC Mobile Measurements in Baltimore and Washington, DC
Black Carbon (ng m-3)
Baltimore
DC-Baltimore
Washington, DC
Hot colors indicate where NOAA’s ARC frequently observed high concentrations.
Washington, DC
Black Carbon (ng m-3)
Baltimore
Baltimore

## Slide 4: Air Quality and Environmental Justice
Need to inform EJ efforts
MDE is collaborating with several community organizations throughout the state to look at community-scale needs
Sensors are a big part, but large-scale research / satellites can play a big role
MDE is collaborating NESDIS and Dr. Shobha Kondragunta on the ongoing impact of the Key Bridge Collapse and use of satellites by state agencies
  EJ / Sensors
  Credit: Zigang Wei

## Slide 5
Curtis Bay Neighborhood
from NOAA’s ARC 4/27/2023
~Equal truck traffic
Black Carbon (BC) (µg m–3)
Pennington Curtis
Ave. Ave.
95th 10.9 1.8
Mean (s) 2.1 0.7
Median 0.8 0.5
5th 0.2 0.1
BC measurements offer insight:
  High overall
  Pennington Ave. >> Curtis Ave.
Due to stop-and-go traffic: turbo-lag.
ARC Measurements in Curtis Bay

## Slide 6: Deriving Hourly CO2 Emissions using TEMPO NO2 as a Proxy
ECO2 = ENOx * RatioCO2/NOx
ECO2 = ENOx * RatioCO2/NOx
km
Derive CO2 emissions for top 50 urban areas in the US (population > 1 million) with winds from GOES, CO2M and GOSAT-GW CO2/NO2 ratios
Using high spatial resolution mobile observations of CO2 and NO2 to validate estimates of TEMPO CO2
Mobile NOx vs. CO2 on I-95

## Slide 7
Takeaways
NOAA’s ARC mobile lab serves as an effective tool for studying air quality, greenhouse gases, and environmental justice in urban environments.
The high spatial resolution measurements obtained from the ARC mobile lab can enhance the evaluation of TEMPO and GEOXO satellite observations.
Ratios of species measured by the mobile lab can be used to derive emission rates and assess the accuracy of emission inventories.