## Slide 1: 4b. CCOR GPA Development Overview
A. Thernisien, NRL
SWFO PGD PDR, August 30, 2021

## Slide 2: CCOR Science
Observe coronal mass ejections (CMEs), in particular halo CMEs
Determine their direction, and speed based on model
  Ice cream cone, GCS, …
Estimate CME mass
Estimate time arrival at Earth
CCOR Performance Requirements
  CCOR-1 (GOES-U): from 3.7Rsun to 17Rsun, Earth, 50arcsec resolution
  CCOR-2 (SWFO-L1): from 3.0Rsun to 22Rsun, L1, 70arcsec resolution
Cadence: one 2k x 2k image every 15 minutes
Latency: <12min transfer to spacecraft
Photometric accuracy: <10%
Requirement documents: Performance Operational Requirement Document (PORD)
  CCOR-1: SSD-RQT-CC007 Rev. A
  CCOR-2: SSD-RQT-CL004 Rev. -
SWFO PGD PDR, August 30, 2021
R: 4.13, 4.15; C: SDD

## Slide 3: CCOR Performance Requirements
SWFO PGD PDR, August 30, 2021
Specifications | Requirements | 
 | CCOR-1 | CCOR-2
Requirement Doc. (PORD*) | SSD-RQT-CC007 Rev. A | SSD-RQT-CL004 Rev. -
Spacecraft | GOES-U | SWFO-L1
Bandpass | WL: 450-750nm | WL: 450-750nm
FOV | 3.7 to 17 Rsun | 3.0 to 22 Rsun
Spatial resolution | 50 arcsec | 70 arcsec
Image size | 2048x1920 pixels | 2048x1920 pixels
Cadence | 15 min | 15 min
Latency | < 12 min | ≤ 18 min
Photometric accuracy | < 10 % | < 10 %
Minimum corona intensity | ≥1.0e-11 Bsun | ≥1.0e-11 Bsun
* PORD: Performance Operational Requirement Document
R: 4.13, 4.15; C: SDD

## Slide 4: CCOR As Built Specs
SWFO PGD PDR, August 30, 2021
Specifications | Requirements | 
 | CCOR-1 | CCOR-2
Requirement Doc. (PORD*) | SSD-RQT-CC007 Rev. A | SSD-RQT-CL004 Rev. -
Spacecraft | GOES-19 | SWFO-L1
Bandpass | WL: 450-750nm | WL: 450-750nm
FOV | 4.1 to 20 Rsun | 3.4 to 25 Rsun
Spatial resolution | 40 arcsec | 65 arcsec
Image size | 2048x1920 pixels | 2048x1920 pixels
Cadence | 15 min | 15 min
Latency | < 12 min | ≤ 18 min
Photometric accuracy | < 10 % | < 10 %
Minimum corona intensity | <1.0e-11 Bsun | <1.0e-11 Bsun
* PORD: Performance Operational Requirement Document
R: 4.13, 4.15; C: SDD
Allocated from requirement for total latency to user (both CCORs): < 30 min
Slide added in January 2025